## Slide 1: Defining Storage Use Cases
IPWG Meeting
July 18, 2017

## Slide 2: Need for Defining Use Cases
Important to define use cases as we begin developing the Policy (including compensation) and Technical requirements for storage systems
Important to initiate the dialogue early so that we are not being reactionary, and can plan for near term interconnections
The use cases may evolve over time and Policy and Technical requirements will need to be able to quickly adapt to these changes
Use cases may need to be segregated by compensation method (NEM vs Value Stack)
Technical requirements for DC versus AC coupled systems may need to be different

## Slide 3: Residential/Commercial Behind the Meter Storage
Behind the meter storage coupled with DG system and storage charged with DG and net generation no higher than DG application
Behind the meter storage coupled with DG system and storage not limited to being charged by DG
Behind the meter stand alone with no increase in demand (off peak charging) and no net generation (or controls included so no export)
Behind the meter stand alone with increase in demand or net generator (export)

## Slide 4: Coupled with Stand Alone DG System (CDG or RNM installation)
Never acts a load (charged exclusively from the DG system) and net generation no higher than DG application
Storage system does or can act as a load (charged by the distribution system)
  Only charged during non-peak hours
  No limitation on charging

## Slide 5: Stand Alone Storage System
System not coupled with existing customer load or DG system
System acts as both a load and a generator as seen by the distribution system
Commercial installation with small load and large storage system. Potential for large export due to storage. Can effectively be viewed as a stand alone system.
Notes: i.e. – 1 MW Load, 5 MW battery.