## Slide 1
2019 Summer Preparedness
May 16, 2019

## Slide 2: 2019 Summer Preparedness New York State Electric System Preparedness

## Slide 3: Historical Actual, Normal, & Forecast – Summer Peak(MW)
Source: NYISO
Chart: Actual, Normal, & Forecast - Summer Peak (MW) NYCA Base Case - With Energy Program Impacts
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Actual | 32433 | 30845 | 33453 | 33867 | 32439 | 33956 | 29782 | 31139 | 32075 | 29699 | 31861
Normal | 33670 | 33065 | 33452 | 33019 | 33106 | 33497 | 33291 | 33226 | 33225 | 32914 | 32512
2016 Forecast | 33360 | 33363 | 33404 | 33477 | 33501 | 33555 | 33650 | 33748 | 33833 | 33926 | 34056
2017 Forecast | 33178 | 33078 | 33035 | 32993 | 33009 | 33034 | 33096 | 33152 | 33232 | 33324 | 33398
2018 Forecast | 32904 | 32857 | 32629 | 32451 | 32339 | 32284 | 32276 | 32299 | 32343 | 32403 | 32469
2019 Forecast | 32382 | 32202 | 32063 | 31971 | 31700 | 31522 | 31387 | 31246 | 31121 | 31068 | 31115

## Slide 4
Forecast Impact on Summer Peak Demand (MW) of
Energy Efficiency and Distributed Generation
Source: NYISO
Chart: Energy Program Impacts - Summer Peak (MW) NYCA
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Energy Efficiency | 228 | 495 | 751 | 1003 | 1293 | 1546 | 1871 | 2198 | 2474 | 2692 | 2895
Distributed Generation | 766 | 903 | 1060 | 1169 | 1266 | 1355 | 1425 | 1485 | 1539 | 1583 | 1622

## Slide 5: 2019 Summer Capability
 | 2018 | 2019
Installed Generation Capacity | 39,325 | 39,295
Demand Response – Special Case Resources (SCRs) | 1,219 | 1,309
Total NY Control Area (NYCA) Internal Capability | 40,544 | 40,604
Net Firm Purchase Imports | 1,625 | 1,452
Total Capability | 42,169 | 42,056
Source: NYISO

## Slide 6: NYS Peak Demand and Installed Reserve Margin
 | Forecast
Demand Forecast | 32,382 MW
17% Required Installed Reserve Margin (IRM) | 5,505 MW
Total Capability Requirement | 37,887 MW
Total Capability This Summer | 42,056 MW
Surplus (Capability Above Requirement) | 4,169 MW
Capability Versus Demand Forecast (%) | 129.9%
Source: NYISO

## Slide 7: Utility Load Relief Programs
Chart: DLRP= 366 MW, CSRP= 607 MW & DLC= 106 MW Total 1,079 MW
| CHG&E | ConEd | National Grid | NYSEG | O&R | PSEG-LI | RG&E
DLRP | 366
CSRP | 9 | 325 | 222.48 | 25.913 | 20 | 4.977
DLC | 14 | 25 | 6.6 | 2.8 | 49 | 8.711
DLRP – Distribution Load Relief Program
CSRP – Commercial System Relief Program
DLC – Direct Load Control Program

## Slide 8: Utility Transmission and Distribution Systems Preparedness
Surveys - Discussed responses to preparedness survey with each utility
Work - All planned reinforcements, inspections, and repairs are or will be completed
Spares - Each utility has adequate spare equipment on hand
Planned Outages - Major generator and transmission planned outages require NYISO approval, and are avoided during peak periods
Meeting Demand - Each utility expects to meet peak demand with all lines and generators in service
Meeting Criteria - Each meets NPCC and NYSRC operating criteria
Mitigation – NYISO and each utility have operating procedures to mitigate reliability issues

## Slide 9: 2019 Summer Preparedness New York State Electric Portfolio, Volatility, and Supply Price Outlook

## Slide 10
Chart: NYISO Spot Market vs. Utility Full Service Residential Customer Supply Portfolio Volatility (Statewide 12-month rolling average)

## Slide 11
Chart: New York State Electric Supply Portfolio Full Service Residential (Summer 2019)
| Fixed Price | Market Price | Unhedged Generation | Index Price
 | 0.59339 | 0.27322 | 0.024794 | 0.10859

## Slide 12
Chart: Average Energy Price Comparison Summer Season
| NY West LBMP ($/MWH) | NY Hudson Valley LBMP ($/MWH) | New York City LBMP ($/MWH)
NYMEX Futures June-September, 2019 | 32.7775 | 31.785 | 34.2725
Average Day-Ahead Market June-September, 2018 | 33.1125 | 32.555 | 35.4025
NYMEX Futures June-September, 2018 | 28.1125 | 28.67 | 31.5175

## Slide 13
Chart: Statewide Weighted Average Full Service Residential Supply Price - Summer Months (Cents per kWh)
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 7.8186 | 8.2651 | 8.5386 | 7.2345 | 6.8047 | 6.8639 | 6.6728

## Slide 14
Chart: NYCA SUPPLY COSTS 2006-2018
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Energy and Ancillary | 12.403 | 13.4358 | 15.7995 | 7.7294 | 9.637 | 9.2232 | 7.3735 | 9.6539 | 11.0921 | 7.8524 | 5.5 | 5.7 | 7.2
Capacity | 2.1004 | 2.1861 | 1.3699 | 1.3959 | 1.5342 | 0.84383 | 1.4251 | 2.701 | 3.326 | 2.6295 | 2.1 | 1.8 | 1.8
Gas Price | 7.75 | 8.09 | 10.85 | 5.26 | 5.73 | 5.56 | 3.95 | 5.26 | 5.46 | 3.51 | 2.76 | 3.44 | 3.89