## Slide 1: INTERCONNECTING STORAGE IN NEW YORK

## Slide 2: DISCUSSION AGENDA
IPWG Storage objective
  Draft SIR language providing a pathway for the study of solar + storage and standalone storage systems in New York.
Update on storage discussion and objectives underway at the ITWG
  Clarify study parameters (export capacity vs. aggregate).
  Define control standards and practices for ensuring system performance complies with approved operating standards.

## Slide 3: THRESHOLD ISSUE
Solar + Storage should qualify for the SIR and distributed generation tariffs based on the export capability at the point of common coupling (PCC), not the aggregate nameplate rating of the generator (i.e. solar inverter) and storage units.
Standalone storage should qualify for the SIR based on the export capability at the point of common coupling (PCC), not the aggregate nameplate ratings of the units within the facility.
Solar + Storage should be studied based on net export and not based on aggregate nameplate capacity.

## Slide 4: KEY INPUTS & CHARACTERISTICS FOR INTERCONNECTION ANALYSIS OF STORAGE
Generation capacity / max injection (export / non export)
Load / grid charging scenarios

## Slide 5: EXPORT CAPACITY AND LOAD STUDIES ACCOMMODATE ALL USE CASE SCENARIOS
The following slides outline each of the use case scenarios identified by the JU and how they could be accommodated in the SIR based on an export/load delineation.
This high level approach can adapt to evolving policy signals and electricity load needs to maximize the State’s ability to meet our clean energy goals

## Slide 6: USE CASES
No additional load - non-exporting (DG-charged storage reduces onsite demand)
  Behind the meter storage coupled with DG system. Storage charged with DG. Net generation no higher than DG application
  CDG/RNM solar. Never acts as load. Charged exclusively from the DG system. Net generation no higher than DG application
No additional load – exporting (DG-charged storage exports to grid as signaled by optimal compensation)
  Commercial installation with small load and large storage system. Potential for large export due to storage.

## Slide 7: USE CASES
Additional load / non-exporting (DG and/or off-peak grid-charged storage reduces onsite peak demand)
  Behind the meter storage coupled with DG system and storage not limited to being charged by DG
  Behind the meter stand alone with no increase in demand (off peak charging) and no net generation (or controls included so no export)
Additional load / exporting (DG and/or grid-charged storage exports to offset peak demand)
  Behind the meter stand alone with increase in demand or net generator (export)
  Storage system does or can act as a load (charged by the distribution system) and only charges during non-peak hours
  Storage system does or can act as a load (charged by the distribution system) with no limitation on charging

## Slide 8: USEFUL LINKS
California PG&E Storage page
CPUC Rule 21 Interconnection