## Slide 1
Valuing Air Pollutant Externality Benefits from Distributed Energy Resources
Jeffrey Shrader, Ph.D.
Burcin Unel, Ph.D.
Avi Zevin

## Slide 2: Outline
Basic principles and methodology
Methods and data needs
Examples
Summary

## Slide 3: Distributed Energy Resources and Externalities
Pollution imposes costs on society that are not borne by the polluters themselves
Internalize environmental externalities
  Polluter pays a tax based on those damages; or
  Other resources are paid for the damage that they avoid
The Commission can increase economic efficiency by directly incorporating the monetary value of avoided emissions into the value stack in the Value of Distributed Energy Resources Proceeding

## Slide 4: Principles
DERs should be compensated for uninternalized damages they avoid
“E” value should depend on:
  Location: DER worth more when avoiding air pollution in areas with high population density and more vulnerable population
  Time: DER worth more when higher emitting generators are on the margin
  Pollutant: Different pollutants cause different levels of public health and climate damage
For emitting DERs, “E” value should be reduced based on their emissions and could potentially be negative
Payment should balance accuracy and administrability

## Slide 5: Methodology
Goal: To calculate environmental value of each kWh of DER generation to be added to DER value stack
Methodology: 5 steps, updated as often as feasible:
Identify the generator that is displaced by DER
Calculate emission rates (kg/kWh) of the displaced resource and DER
Calculate the damage per unit ($/kg) of avoided emissions and DER emissions (if any)
Monetize the value of avoided damage from displaced generation ($/kWh)
Net the damages avoided by DER and damages from DER itself (if any)

## Slide 6: Step 1: Identify the Generation Resource that Is Displaced
Illustrative Dispatch Curve

## Slide 7: Step 1: Identify the Generation that Is Displaced by DER
A counterfactual ISO run
Assume that each kWh of DER displaces a kWh of the marginal resource in a particular geographic region/time
  Assumption: DERs do not change the marginal resource
  Regional analysis is important when congestion is high
Approach to Avoid: Grid Average
  Misses temporal/regional variation
  Does not guarantee that DERs truly avoid emissions

## Slide 8: Step 2: Calculate Emission Rates (kg/kWh) for Displaced Generation Resource and DER
Historical average emission rates readily available from EPA for large generators
  Updated every 3 years.
  Greater than 25 MW
Smaller, newer generators may require assumed rates based on fuel input, design efficiency, existing/use of pollution control equipment
Emission rates also vary over time, due to equipment aging, capacity factor changes, and weather
  Engineering estimates
  Regression estimates like Graff Zivin (2014)

## Slide 9: Step 2: Data Needed to Calculate Emission Rates
Category | Pollutant | Data Source (latest data year)
Criteria Air Pollutants | SO2, NOx | EPA eGrid (2014): plant-level emission rates for steam units > 25MW; CT, CC, & ICE online after 1990
 | PM2.5 (direct) | National Emissions Inventory (2014): plant-level annual emissions National Energy Technology Laboratory (2010): Technology-based emission factors for NGCC AP-42 (2011): estimate of natural gas and petrol steam turbines and combustion turbines. NY DEC
GHGs | CO2, N2O | eGrid (2014)
Potential Emissions Data Sources

## Slide 10: Example: Average Emission Rates Based on Fuel Type
Chart: Gas Plant
| Carbon Monoxide | Nitrogen Oxide | Particulate Matter 10 | Particulate Matter 2.5 | Sulfur Dioxide | Volatile Organic Compounds
 | 0.097466 | 0.53411 | 0.2768 | 0.26316 | 0.02924 | 0.083821
Chart: Dual Fuel Plant
| Carbon Monoxide | Nitrogen Oxide | Particulate Matter 10 | Particulate Matter 2.5 | Sulfur Dioxide | Volatile Organic Compounds
 | 0.58038 | 0.5345 | 0.073853 | 0.067512 | 0.39351 | 0.037673

## Slide 11: Example: Grid-wide Estimated Hourly Emissions Rate for SO2 in Eastern Interconnection Region
Source: Graff Zivin et. al (2014)
Chart: Time of day
| 1:00 | 2:00 | 3:00 | 4:00 | 5:00 | 6:00 | 7:00 | 8:00 | 9:00 | 10:00 | 11:00 | 12:00 | 13:00 | 14:00 | 15:00 | 16:00 | 17:00 | 18:00 | 19:00 | 20:00 | 21:00 | 22:00 | 23:00 | 24:00
Marginal SO2 emission rate | 13.442 | 13.618 | 13.574 | 13.442 | 13.112 | 11.99 | 10.406 | 9.592 | 9.57 | 9.746 | 9.482 | 8.888 | 8.382 | 8.008 | 7.832 | 7.744 | 7.744 | 7.832 | 7.964 | 8.118 | 8.47 | 9.284 | 10.846 | 12.43
Lower CI | 12.709 | 12.8418 | 12.7547 | 12.6227 | 12.3358 | 11.257 | 9.6298 | 8.859 | 8.837 | 9.0561 | 8.749 | 8.0256 | 7.4765 | 7.0594 | 6.8402 | 6.7522 | 6.7522 | 6.9696 | 7.231 | 7.4281 | 7.7801 | 8.5941 | 10.1992 | 11.7832
95% Confidence Interval | 14.175 | 14.3942 | 14.3933 | 14.2613 | 13.8882 | 12.723 | 11.1822 | 10.325 | 10.303 | 10.4359 | 10.215 | 9.7504 | 9.2875 | 8.9566 | 8.8238 | 8.7358 | 8.7358 | 8.6944 | 8.697 | 8.8079 | 9.1599 | 9.9739 | 11.4928 | 13.0768

## Slide 12: Step 3: Calculate Damage per Unit of Emissions ($/kg)
CO2 is a global pollutant so damage calculation is straightforward by using the Interagency Working Group’s Social Cost of Carbon
For other pollutants, damage per unit of emissions is a function of:
  Location
    Air transport
    Population density
    Ambient concentration
    Local population health status
  Time
    Ozone is a daytime, seasonal pollutant
  Pollutant
    Each pollutant has a different damage function
    Secondary pollutants (PM2.5, ozone) are formed by combinations of other pollutants

## Slide 13: Step 3: Tools to Calculate Damage per Unit of Emissions
Tool | Geographic Granularity | Add’l Data Needed | Pollutants Covered | Notes | Source
Custom model | Variable | High | ozone (NOx,VOC), PM2.5 (directly emitted PM2.5, NOx, VOC, SO2), air toxics | Geographic-specific damage estimates based on: Air transport Ambient concentrations Population, Comorbidity | Bay Area Air Quality Management District (2017)
EASIUR | 36 km | Low | SO2, NOx, NH3, PM2.5 | Detailed air transport model Easy calculation of location and time specific emission damage Seasonal variation | Heo, Adams, and Gao (2016)
BenMAP | High (default); Variable (custom) | Medium (default); Varies (custom) | ozone, PM2.5 | Translates all pollutants into secondary PM & ozone; Driven primarily by mortality; Can input own data | U.S. EPA
AP2 | County | Low | SO2, NOx, VOC, NH3, PM2.5, PM10 | Accounts for air transport Broader monetized damage categories | Muller, Mendelsohn, Nordhaus (2011)
COBRA | State or county | Low | PM2.5 (directly emitted PM2.5, NOx, VOC, SO2) | Recently updated (2017) Previously used by NY PSC Accounts for air transport Driven primarily by mortality | U.S. EPA (2017)

## Slide 14: Examples of Damage Per Unit of Emissions
Dollar value of average damage per kg
Pollutant | 2016 EPA RIA | DPS | Bay Area
SO2 | $40 to $91 per kg | $27 per kg | $39 per kg
NOx | $10 to $40 per kg | $13 per kg | $8 per kg
PM2.5 (direct) | $175 to $400 per kg |  | $500 per kg

## Slide 15: Example: Locational Variation in Damages
Source: NYC Department and Health of Mental Hygiene Bureau of Environmental Surveillance and Policy (2013)

## Slide 16: Step 4: Monetize the Avoided Externality from Displaced Generation ($/kWh)
Take into account any existing policies that partially internalize the damages
  Carbon charge, RGGI, Cross-state air pollution rule (CSAPR)
Calculate the monetized value of avoided damages per unit of displaced generation for each pollutant
  Multiply the results of Step 2 and Step 3

## Slide 17: Example: Avoided CO2 damages per unit of generation from a displaced gas generator
Emissions rate =
Uninternalized damage rate =
CO2e monetized value =

## Slide 18: Example: Monetized Values for a Non-emitting DER
Pollutant | 2016 EPA RIA | DPS | Bay Area
SO2 | $76 to $171 per MWh | $52 to $55 per MWh | $77 per MWh
NOx | $4 to $12 per MWh | $5 per MWh | $3 per MWh
PM2.5 | $7 to $16 per MWh |  | $22 per MWh
Dollar value of average damage per MWh

## Slide 19: Step 5: Monetize Net Damages
If the DER does not emit, then the monetized value is given by the previous step
For emitting DER, monetized value of DER emissions must be subtracted from the amount calculated in Step 4
  If the DER creates more damage than it avoids, then the “E” value should be negative

## Slide 20: Example: Monetized Net Avoided Damage for Non-emitting DER
Example Values for Three Cities: Gas on the Margin

## Slide 21: Example: Monetized Net Avoided Damage for Non-emitting DER
Example Values for Three Cities: Dual Fuel on the Margin

## Slide 22: Summary of Methods and Necessary Data
Identify the resource displaced by distributed generation
    Most granular: Counterfactual generation with and without DERs
    Alternative: Marginal generator (can vary with zone based on congestion)
Calculate emission rates
    Most granular: Real-time emission rates for all pollutants
    Alternatives: Historical data, engineering or econometric estimates
Calculate damages per unit of emission
    Most granular: Pollution transport, affected population, ambient concentration, comorbidity
Monetize the avoided damage from displaced emissions
    Existing policies should be taken into account
Monetize net avoided damage from DERs

## Slide 23: Bottom Line
Externalities should be internalized
The value of net avoided emissions is not zero
This value changes with respect to time and location
We have good, existing research and tools to be able to do this calculation
The method can get more granular as more tools and data become available