## Slide 1: Shaped E Value
July 11, 2018
Stefanie Tanenhaus

## Slide 2: Contents
Background & Methodology
Locational Hourly Marginal Emissions Rates and Prices
Storage Simulations
  Approach
  Results
Summary

## Slide 3: Shaped E Value and Storage Modeling Approach
Use historical and 2030 NYISO marginal emissions rate (MER) data to design and test Environmental (E) value signals
Calculate carbon savings and revenue potential under different E value shapes for different DERs (solar and storage)

## Slide 4: Marginal Emissions Rate Data & Methodology
Hourly 2015-16 Marginal Emissions Rate (MER) provided by NYISO/Brattle using Marginal Units Dispatch Methodology
Assumptions:
  During intervals when a zone has multiple marginal units, simple average used.
  If there is just a single NYCA-wide marginal unit, Brattle Group assigned its emissions rate to all zones.
  Assumed a marginal carbon intensity of zero when large hydro is marginal in very low-priced hours (LBMP < $10/MWh). For higher-priced hours marginal carbon intensity based on the average marginal emissions rate of periods with similar LBMPs
Notes: If there is one marginal unit in Upstate Zones (A-E) and one marginal unit
in Downstate Zones (F-K), all Upstate Zones are assigned the Upstate
marginal unit and all Downstate Zones are assigned the Downstate
marginal unit
If there is more than one marginal unit in Upstate Zones (or Downstate
Zones), Brattle Group assigned Zones without marginal units to the
marginal unit in adjacent alphabetical zones (i.e., for Upstate Zones, A-
>B->C->D->E and then the same in reverse as necessary).

## Slide 5: Illustration of Peak and Off-Peak E Value
Figure visualizes a seasonal peak/off-peak E Value vs. the current flat E Value as determined using historical MERs. As can be seen in the off-peak season, the off-peak E Value is lower than the current flat E Value, while the peak value is slightly higher. In the peak season both the off-peak and peak E Values are higher than the current flat E Value.

## Slide 6: MERs and Hourly E Value Heat Maps 2015-6 Average MERs for Statewide
Statewide
2015-16
Seasonal Average Shaped E Values | Oct-Dec, March-May | Jun-Sept, Jan-Feb
Peak | $27.82 | $31.74
Off-Peak | $25.55 | $27.74

## Slide 7: MERs and Hourly E Value Heat Maps 2030 Base Case Average MERs from Acelerex Study
Seasonal Average Shaped E Values | Oct-Dec, March-May | Jun-Sept, Jan-Feb
Peak | $26.71 | $38.48
Off-Peak | $15.41 | $30.10
Statewide
2030
Notes: Peak shifts to later in the day

## Slide 8: Environmental Value Approach
Averaged 2015 and 2016 NYISO/Brattle marginal emission rates (MERs)
  No day-type or weather adjustment
Used MERs to shape E value
Averaged upstate zones (A-I) and downstate zones (J-K)
Defined daily peak windows of 2 PM-7 PM to develop TOU like peak and off-peak E values
Defined seasonal peak months of Jun-Sept and Jan-Feb
Modeled energy storage carbon savings and values under current and future conditions

## Slide 9: Shaped E Value Example- Peak/Off-Peak Seasonal
Peak Period: 2pm-7pm
Peak Months: Jun-Sept + Jan-Feb
Flat E Value $27.41
  Flat E Value is scaled based on MERs during Peak/Off-Peak Periods
  MER % = GHG shape contribution, or fraction of emissions that occur during time & month windows
Result is that E Value x MER % summed for each period/month window equals Flat E Value

## Slide 10: Seasonal Peak / Off-peak ‘E’ Value Statewide 2015-2016 Data
 | Peak Period (2 pm– 7 pm) |  | Off-Peak Period (8 pm – 1 pm) | 
 | March-May+ Oct-Dec | Jun-Sept + Jan-Feb | March-May+ Oct-Dec | Jun-Sept + Jan-Feb
MER (%) | 12.9% | 14.4% | 35.2% | 37.6%
MCI (MT CO2 / MWh) | 0.518 | 0.587 | 0.472 | 0.512
Price ($/MWh) | $27.88 | $31.59 | $25.38 | $27.55
Equations
$27.41 (Flat E)= 12.9%*$27.88 + 14.4%*$31.59+35.2%*$25.38+37.6%*$27.55
$27.88 / $31.59 = 0.518 / 0.587
$27.88 / $25.38 = 0.518 / 0.472
$27.88 / $27.55 = 0.518 / 0.512

## Slide 11: Storage Can Reduce Emissions Under Certain Conditions
Storage reduces emissions if:
  Storage charges with low emission electricity, and discharges to displace higher emissions electricity and
  The roundtrip efficiency of storage is high enough not to offset the emissions delta
Storage increases emissions when:
  Emissions rates, losses and charging behavior lead to inefficient battery operation
  Electricity prices are not aligned with emissions rates and do not include the cost of carbon
Profit-maximizing energy storage often results in increased emissions today
Including a carbon price signal or internalizing the cost of carbon into electricity prices can result in more beneficial storage behavior

## Slide 12: With today’s MERs there is limited potential for stand-alone storage to reduce emissions
 | Storage |  | Solar |  | Solar + Storage | 
 | ∆ Emissions (tons) | Revenues ($) | ∆ Emissions (tons) | Revenues ($) | ∆ Emissions (tons) | Revenues ($)
Seasonal Peak/Off Peak | 0 | $0 | -2,790 | $142,445 | -2,790 | $142,445
Annual Peak/Off Peak | 0 | $0 |  | $142,294 | -2,790 | $142,294
Annual Hourly E | -191 | $10,337 |  | $150,890 | -2,879 | $155,662
Battery Size: 1 MW, 4 hour

## Slide 13: Storage Dispatch with Shaped Hourly E Value Signal
Storage charges when E value/MER is low and discharges at high values  Emissions savings and increased revenues

## Slide 14: 2030 Emissions Savings Potential Increases with Higher Renewables
 | Historical |  | Acelerex 2030 |  | LBNL Balanced |  | LBNL High Wind |  | LBNL High Solar | 
 | ∆ Emissions (tons) | Revenues ($) | ∆ Emissions (tons) | Revenues ($) | ∆ Emissions (tons) | Revenues ($) | ∆ Emissions (tons) | Revenues ($) | ∆ Emissions (tons) | Revenues ($)
Annual Hourly E Value | -191 | $10,337 | -678 | $56,848 | -782 | $46,690 | -743 | $44,344 | -816 | $46,469
Results represent upper bound on emissions (E Value is only price signal) for energy storage only
Battery Size: 1 MW, 4 hour

## Slide 15: Zone A MERs and Energy Prices are Relatively Aligned
 | Zone A |  |  | 
Price Signal | ∆ Emissions (tons) | GHG Revenues ($) | Energy Revenues ($) | Total ($)
LBMP Only | (43) | $2,860 | $13,362 | $16,222
E Value Only | (228) | $15,041 | $834 | $15,874
LBMP + E Value | (184) | $12,146 | $10,074 | $22,220
Battery Size: 1 MW, 4 hour; Round-trip Efficiency (RTE): 85%
Simulation Results in Zone A Historical MERs, LBMP + E value
Notes: Solar only flat E value: $142,451

## Slide 16: Zone J Energy Prices are Higher and More Volatile
 | Zone J |  |  | 
Price Signal | ∆ Emissions (tons) | GHG Revenues ($) | Energy Revenues ($) | Total ($)
LBMP Only | (4) | $216 | $24,777 | $24,993
E Value Only | (127) | $7,287 | $5,535 | $12,821
LBMP + E Value | (65) | $3,719 | $23,248 | $26,967
Battery Size: 1 MW, 4 hour; Round-trip Efficiency (RTE): 85%
Simulation Results in Zone A Historical MERs, LBMP + E value
Relative to energy prices, E value in Zone J provides lower opportunity for revenues

## Slide 17: Key takeaways
Hourly MERs are noisy and vary year by year but the average peak/off-peak ratios are fairly stable
  This supports the proposed peak/off-peak approach
Going to peak window with a shorter window (4-8 hours) makes sense because the system may change over time but a shorter peak window will probably continue to capture the emission peak
  E value should evolve as system changes
For non-storage, i.e. solar, technologies they can have the option to opt-into a shaped or flat E
  Shaped E is better aligned with solar production and results in more revenue
For storage a simple peak/off-peak differential (adjusted for efficiency losses) might be the best solution since if the peak window is short enough we can assume they never charge during it
No matter what E signal is sent it is not expected to be a large benefit under current system conditions
However, when there is more zero marginal emission rate resources on the system there will be increasing emission benefits

## Slide 18: California GHG Signal Approach
California Self-Generation Incentive Program (SGIP) incentivizes DERs (including energy storage systems)
Legislation (SB 861) directs regulators to impose operational requirements to on energy storage systems to ensure GHG emissions reductions in addition to customer benefits
Options explored:
  Minimum cycling requirement
  Prohibit charging/discharging during certain windows
  Updated TOU rate approaches
  GHG dispatch signal

## Slide 19: California GHG Signal Takeaways
Operational Constraints:
  Parasitic losses have a big impact for low utilization storage.
  Limiting charging and discharging during certain windows does not necessarily result in net GHG reductions.
  Requiring a minimum capacity factor or number of cycles for year tends to increase rather than decrease GHG
Price Signals:
  A price based signal was not substantial enough compared to bill reduction benefits for customer.
  New TOU rates were better than old rates, but had mixed results, varied significantly by customer type and rate.
  A GHG signal combined with a minimum RTE requirement is far superior for achieving GHG reductions, with limited cost impacts for customers (e.g. bill impacts for cycling degradation).
Preliminary recommendations of requirements for parasitic losses below 3%, minimum RTE of 85%. However, E3 has also found that even low RTE systems can provide net GHG reductions with a GHG signal.

## Slide 20: appendix

## Slide 21: Top 100 Peak Carbon/E Value Hours 2015-6 Average MERs for Statewide
Statewide
Only top 25 hours shown below

## Slide 22: Top 100 Peak Carbon/E Value Hours 2030 Base Case Average MERs from Acelerex Study
Only top 25 hours shown below
Statewide

## Slide 23: Top 100 Peak Carbon/E Value Hours 2030 Base Case + Storage Average MERs from Acelerex Study
Only top 25 hours shown below
Statewide

## Slide 24: GHG-neutral REC (Peak vs Off-Peak) Zone A - example
Peak period (7 am-10 pm)
  On-Peak average GHG intensity = 0.452 MT CO2 / MWh
  On-Peak Wind generation share = 62.1%
Off-Peak period (11 pm-6 am)
  Off-Peak average GHG intensity = 0.273 MT CO2 / MWh
  Off-Peak Wind generation share = 37.9%
REC price = $24.24/MWh
  Peak period = $28.52/MWh
  Off-peak period = $17.22/MWh
62.1%*28.52 + 37.9%+17.22 = $24.24

## Slide 25: Overview of Original E3 MER Methodology
Implied GHG Marginal Emission Rates (MERs) based on Implicit Marginal Heat Rate Method Derived from LBMP data
  We imposed caps in regions at the lower/upper LBMP range to account for marginal zero emission resources at the lower end and marginal must-run/reliability units at the upper end
  Need to confirm that lower-capped regions are renewables or “use it or lose it” hydro
  Conservative approach for higher capped regions which may understate emission reductions if there is dual fuel or oil fired peakers on the margin
    However, for upper-capped regions, change in behavior is unlikely if these are must-run or other reliability units that cannot be backed down

## Slide 26: Marginal Emission GHG Signal Implicit Marginal Heat Rate (IMHR) Method
Inputs - 2017 Data
  NYISO DAM & RT LMP (Zones A & J)
  Gas Prices from SNL
    Zone A – Dominion North
    Zone J – Transco Z 6
    Zone G – Iroquois Z 2 + Millennium
  RGGI Prices – 2017 Auction Results
Assumptions:
Parameter | Value | Units | Source
Delivery Adder | 0 | $/MMBtu | N/A
Social Cost of Carbon | 40 | $/metric ton | N/A
Emission Factor (CC of Gas) | 0.0531 | MT / MMBtu | EIA 2017
Non-fuel Variable O&M | 2.00 | $/MWh | SNL Financial Supply Curve 2017
Minimum Heat Rate | 5,500 | Btu/kWh | SNL Financial Supply Curve 2017
Maximum Heat Rate | 12,000 | Btu/kWh | SNL Financial Supply Curve 2017